To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Modul’Up Compact Wood. Part of the Modul’Up adhesive free sheet vinyl collection of heterogeneous project vinyl floor coverings.  Its 0.70mm pure PVC wear layer provided with a PUR lacquer offers ease of maintenance and stain resistance. Its unique construction delivers exceptional residual indentation with typical values of 0.02mm for easier movement of rolling loads and indoor wheeled traffic.

Roll width:  2000mm. Thickness:  2.00mm.  Thickness of wear layer:  0.70mm

Colours: - 17 standard colourways

Matching welding rods are available in all collection colours

Consult with Forbo technical literature for details.

150 SHEETING: VINYL

Flooring roll: Heterogeneous PVC to BS EN ISO 10852.

Manufacturer: Forbo Flooring Systems Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912.

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Modul’Up Compact Wood

BS EN ISO 10874 class: 34 / 43
Width: 2000 mm
Thickness: 2.00mm

Colour / pattern: [select from]

8513UP43C | blond chill oak, 8514UP43C | pure chill oak, 8512UP43C | smoked chill oak, 8483UP43C | Scandinavian oak, 8413UP43C | natural oak, 8421UP43C | polar oak, 8412UP43C | grey silver oak, 8420UP43C | clay oak, 8422UP43C | carbon oak, 8224UP43C | brown rustic oak, 8226UP43C | burned charcoal rustic oak, 311UP43C | light grey zebrano, 313UP43C | sand zebrano, 121UP43C | grey linea, 132UP43C | charcoal linea, 9201UP43C | light hybrid wood concrete

Adhesive: Not Required

Seam welding: Hot welding with matching coloured rod. Modul’Up single sided jointing tape should be used to support the seams - refer to manufacturer’s installation guidance.

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polished finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.

770 Skirting

Type: Self coved skirting

Cove former: Quantum Profile Systems reference - 35mm radius tapered to architraves.

Capping strip: Quantum Profile Systems UCS2 PVC capping strip.

Where Modul’up is being installed over existing vinyl asbestos tiles, Quantum Profile Systems combined cove former and capping profiles reference CCF1 is recommended.

Securely bond to background using a plasticiser resistant double-sided tape system or solvent free contact adhesive, with top edge straight and parallel with floor. Accurately mitre at corners.

Turn flooring material up wall, securely bond to cove former and background using a plasticiser resistant double-sided tape system, and ease top of material into edge trim. Accurately mitre at corners. All joints to be hot welded in accordance with the manufacturer’s instructions.

Height: [insert required height] mm

Refer to the manufacturer’s installation guidance for further information.