To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

ColoRex® Plus EC. A high performance loose lay interlocking PVC tile floor covering offering static conductive (electrical resistance 2.5 x 104 to 1 x 106 Ω) performance. Also available to special order as Colorex SD Plus, a static dissipative (electrical resistance 106 to 108 variant. Besides offering ESD/ EMI protection, these Static Control tiles offer high resistance to wear and indentation and have excellent chemical resistance.                                                                                                                   Contact Forbo flooring for further details on availability of Colorex SD Plus.

Dimensions: 607 x 607mm.                                                                                                           Thickness: 10.3mm                                                                                                                                   Colours/ patterns: EC Plus – 6 standard colourways, SD Plus – to order from standard colour range.
Consult with Forbo technical literature for details.

110 TILING: VINYL

Fabricated underlay: N/A

Tiles: Electrostatic and conductive loose lay vinyl
Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk 
Product reference: Forbo ColoRex® Plus. Select either Colorex Plus EC or Colorex Plus SD [to special order].
BS EN 685 class: 34 / 43
Size: 607 x 607 mm.
Thickness: 10.3 mm.
Colour/ pattern: 621001 | Everest, 621004 | montblanc, 621005 | adula, 621007 | quartz, 621013 sahara, 621022 | niagara
Adhesive (and primer if recommended by manufacturer): N/A

Seam Welding: Optional with matching weld cable [delete if not required]

Accessories:
Edging strips as clause 740.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.
An electrical discharge system is required; consult Forbo Flooring for detailed guidance on the requirements of the discharge system.