To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

ColoRex® Plus Basic. A heavy duty adhesive free interlocking PVC floor tile system which provides excellent chemical resistance when conductivity is not required. The floor can also be repaired in case of heavy damage. Colorex Plus Basic is suitable for use in areas with high traffic needing intensive daily cleaning such as shops, stores and warehouses. Suitable when downtime, damp floors or poor sub floors are an issue.

Dimensions: 607 x 607 mm.                                                                                                          Thickness: 10.3mm                                                                                                                                   Colours/ patterns: - 5 standard colourways: 611004 | montblanc, 611005 | adula, 611007 | quartz, 611013 | sahara, 611022 | niagara
Consult with Forbo technical literature for details.

110 TILING: VINYL

Fabricated underlay: N/A

Tiles: adhesive free vinyl
Manufacturer:  Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk 
Product reference: Forbo ColoRex® Plus Basic.
BS EN 685 class: 34 / 43
Size: 607 x 607 mm.
Thickness: 10.3 mm.
Colour/ pattern: As per finishes schedule
Adhesive (and primer if recommended by manufacturer): N/A

Seam Welding: Optional with matching weld cable [delete if not required]

Accessories:
Edging and cover strips, as clause 740.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.