To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Novilon - A range of heterogeneous vinyl coverings, a hard wearing and easy to maintain cushioned floor covering, due to features like Aquagrip, Noviclean and Diamond Seal.

The collection offers an array of beautiful inspiring cushion vinyl floors in a range of designs, including wood, ceramic, concrete and modern allover patterns.

Roll width: 2000/3000/4000 mm.

Thickness: 2.4 mm.

Thickness of wear layer: 0.25 mm.
Colours/ patterns: 53

Cold weld requirements: Consult with Forbo technical literature for details.

150 SHEETING: VINYL

Flooring roll: Heterogeneous PVC to BS EN 653.

Manufacturer: Forbo Flooring Systems Ltd, High Holborn Road, Ripley, Derbyshire, DE5 3NT.  Tel: 0800 0282 162 Fax: 01772 646912.  Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Novilon

BS EN ISO 10874 class: 23 (Domestic Heavy)
Width: 2000/3000/4000 mm.
Thickness: 2.4 mm.
Colour/ pattern: As finishes schedule

Adhesive (and primer if recommended by manufacturer):
Eurocol 640 Eurostar Special – A superior acrylic dispersion low VOC emission adhesive with a high initial grab.
Eurocol 044 Europrimer Multi – Very low VOC emission universal primer.

Seam welding: Cold weld with Forbo Forbo Noviweld 674

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.

Other requirements: Seek advice from Forbo for specific requirements for flooring.