N10 GENERAL FIXINGS/FURNISHING/EQUIPMENT

300 ENTRANCE MATTING

Nuway Flameguard is designed for use in fire risk areas, where the building must comply with the most stringent fire regulations and comprises single Vamac black wiper strips and Non reflective heavy duty aluminium in a closed construction.

Performance:

- Meets the flammability requirements for category ST/ Su/ S Station/ Surface/ Supine.

- London Underground Ltd Engineering Standard 2-010010002 Issue A1: December 2003.

- Tested to BS 476 Part 6 and Part 7, and BS6853:1999:D8.6.

The modules can be fitted into existing or purpose built matwells or can be surface mounted using a purpose made ramp frame

Consult with Forbo Flooring UK Ltd for technical details and to obtain samples.

Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 01773 740 688 Fax: 01773 740 640

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Reference:		Nuway Flameguard

Construction:		Closed

Wiper Strips:		Vamac Rubber

Module:	Single wiper

Scraper Bars:	AN Non reflective heavy duty aluminium

Thickness:	12mm

Size: 			As drawing ref.

Matwell Frame: 	Select required option from:

Existing

Recessed Aluminium AMF216/AMF253/AMF346/AMF506

Ramped Aluminium 12mm ARF 50

Installation: Forbo Flooring recommends that Nuway Entrance systems are installed by a member of the FESSI (Forbo Entrance Systems Specialist Installer) network, details of which can found at the following link www.forbo-flooring.co.uk/FESSI