N10 GENERAL FIXINGS/FURNISHING/EQUIPMENT

300 ENTRANCE MATTING

A range of heavy duty entrance flooring systems for internal and external applications where high point loads or traffic volumes are anticipated. The double sided construction allows the product to be reversed and interchanged to optimise performance and wear. Available closed construction only and 12mm or 17mm thickness.

Tuftiguard HD Design comprises buffed solution dyed wiper strips and Non Reflective heavy duty aluminium scraper bars. For internal use only.
The modules can be fitted into existing or purpose built matwells or can be surface mounted using a purpose made ramp frame.

Consult with Forbo Flooring UK Ltd for technical details and to obtain samples.

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, DE5 3NT

Tel: 01773 740 688 Fax: 01773 740 640

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Reference:		Tuftiguard HD design

Construction:		Closed

Wiper Colour:	Select required option from:/

OC – Ocean / CL – Charcoal / WL – Willow / SC - Scarlet

Wiper Config:	Double

Scraper Bars:		AH - non reflective heavy duty aluminium

Thickness:		12mm / 17mm [Select required option]

Size: 			As drawing ref.

Matwell Frame:	Select required option from:

Existing

Recessed Aluminium AMF216/AMF253/AMF346/AMF506

Ramped Aluminium 12mm ARF 50 / 17mm ARF 70

Installation: Forbo Flooring recommends that Nuway Entrance systems are installed by a member of the FESSI (Forbo Entrance Systems Specialist Installer) network, details of which can found at the following link www.forbo-flooring.co.uk/FESSI