To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Eternal A range of heterogeneous project vinyl coverings, with a high-density calendared top layer, with PUR Pearl™ guaranteeing easy maintenance and a long-lasting sheen.

Forbo’s Eternal Materials collection offers designers an extensive range of designs, all with the same performance specification, reflecting natural materials including Stripe, Stone, Metal and Textile/Woven designs. Selected patterns such as Slate and Textile include surface embossing for a more realistic look.

Eternal design vinyl sheet meets all the functional and practical requirements demanded in such segments as Health and Aged Care, Education, Office, Retail and Leisure & Hospitality.

Roll width: 2000 mm.

Thickness: 2.0 mm.

Thickness of wear layer: 0.7 mm.
Colours/ patterns: 30 colourways

Matching welding rods are available in all collection colours.

Consult with Forbo technical literature for details.

150 SHEETING: VINYL

Fabricated underlay (delete where not required)

Forbo QuickFit Subfloor System. – Optional.
Forbo Sarlibase T.E. Underlay. – Optional                                                                                                    Forbo Vinylbase acoustic underlay – Optional

Flooring roll: Heterogeneous PVC to BS EN ISO 10852.

Manufacturer: Forbo Flooring Systems Ltd, High Holborn Road, Ripley, Derbyshire, DE5 3NT.  Tel: 0800 0282 162 Fax: 01772 646912.  Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Eternal Material

BS EN ISO 10874 class: 34 / 42.
Width: 2000 mm.
Thickness: 2.0 mm.
Colour/ pattern: As finishes schedule

Adhesive (and primer if recommended by manufacturer):
Eurocol 540 Eurosafe Special – A superior acrylic dispersion solvent-free floor covering adhesive with a high initial grab.
Eurocol 640 Eurostar Special – A superior acrylic dispersion low VOC emission adhesive with a high initial grab.
Eurocol 140 Euromix PU – A polyurethane resin and hardener, water-resistant 2-component PU-adhesive.                                                                                                                                                                 Eurocol 233 Eurosol Contact – A synthetic rubber in solvent fast setting contact adhesive.

Seam welding: [select as required]

Hot welding with matching coloured rod.

Cold weld with Forbo Noviweld 671 [optional for flat lay installations only]

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polished finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.

770 Skirting

Type: Self coved skirting

Cove former: ECF4 35mm radius by Quantum Profiles tapered to architraves. Securely bond to base and background using contact adhesive. Accurately mitre at corners.

Top edge trim: UCS2 PVC capping strip by Quantum profiles. Securely bond to background using contact adhesive, with top edge straight and parallel with floor.

Turn flooring material up wall, securely bond to cove former and background using adhesive specified for fixing to base, and ease top of material into edge trim. Accurately mitre at corners. All joints to be hot welded in accordance with the manufacturer’s instructions.

Height: ______