To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

HemingwayDesign x Forbo, uses elements from the standard Marmoleum Modular Shade collection to create three distinct and striking designs.

Marmoleum Modular is an Allergy UK approved floor covering and is made from 88% natural raw materials. 76% of the raw materials are rapidly renewable.

Dimensions: The HemingwayDesign x Forbo collection uses 25x25cm, 50x25cm, 50x50cm and 75x50cm tile elements over the two designs. Snakes and Ladders incorporates additional contrasting coloured 7cm lacing strips and key squares.

Thickness: 2.5 mm.

Colours/patterns – 2 pre-coloured designs – (Snakes and Ladders; The slide – which is available in 3 sizes – 40m2, 20m2 and 10m2)

110 TILING: LINOLEUM

Fabricated underlay: 
Forbo QuickFit Subfloor System. – Optional.

Tiles: Linoleum to BS EN ISO 24011.

Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: HemingwayDesign x Forbo

BS EN ISO 10874 class: 23 / 34 / 42

Design: Snakes and Ladders/ The Slide [select required design]

Thickness: 2.5 mm.

Adhesive (and primer if recommended by manufacturer):

Eurocol 646 Eurostar Premium – A very low emission acrylic dispersion adhesive for linoleum and PVC tile products

Accessories:

Edging and cover strips, as clause 740.

Skirtings, as clause 770.

Finishing: As clause 820 Omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.