To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

130 CARPET TILE:

HemingwayDesign x Forbo Mid Century Weave    Designed for heavy contract use and constructed using 100% regenerated solution dyed ECONYL® polyamide, on a modified bitumen polyester primary and secondary backing. Also available in SOFTbac®. Softbac® is an additional backing layer which also acts as an underlay and offers increased sound and thermal insulation and extends the guarantee period by 50% to 15 years.

Tile size: 50 x 50cm

Pile weight: 796 g/sm ± 10%

Thickness: 7.0mm ± 10%; With SOFTbac® + 3mm ± 10%.

HemingwayDesign x Forbo Mid Century Weave is available in 3 colourways.

HemingwayDesign x Forbo carpet tiles must be laid in accordance with best practice techniques as detailed in the Contract Flooring Association’s guidelines and BS5325.  Consult with Forbo technical literature for further details.

130 CARPET TILE:

Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912;

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: HemingwayDesign x Forbo Mid Century Weave

Type: Textured loop pile

BS EN 1307 classification: Class 33

Level of use class: Heavy Contract

Size: 50 x 50cm

Colour/ pattern: As per finishes schedule

Method of Laying: Quarter Turn/Tessellated (delete as appropriate).

Adhesive: 542 Eurofix Tack Plus.

Accessories: Edging and cover strips, as clause 740.