To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

HemingwayDesign x Forbo printed vinyl is a heterogeneous project vinyl coverings, with a high-density calendared top layer, with PUR Pearl™ guaranteeing easy maintenance and a long-lasting sheen.

The HemingwayDesign x Forbo printed vinyl range offers four imaginative digitally printed visuals which are designed to inspire.

Roll width: 1950mm.  Length; 10m Thickness: 2.0mm.  Thickness of wear layer: 0.7mm.

150 SHEETING: VINYL

Fabricated underlay (delete where not required)

Forbo QuickFit Subfloor System. – Optional.
Forbo Sarlibase T.E. Underlay. – Optional                                                                                                    Forbo Vinylbase acoustic underlay – Optional

Flooring roll: Heterogeneous PVC to BS EN ISO 10852.

Manufacturer: Forbo Flooring Systems Ltd, High Holborn Road, Ripley, Derbyshire, DE5 3NT.  Tel: 0800 0282 162 Fax: 01772 646912.  Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: HemingwayDesign x Forbo printed vinyl

Colour reference: Hopscotch, Hemingbone, Mix & Match and Fresh Cut Graph [select as required]

BS EN ISO 10874 class: 34 / 42.
Width: 1950 mm.
Thickness: 2.0 mm.

Adhesive (and primer if recommended by manufacturer):
Eurocol 540 Eurosafe Special – A superior acrylic dispersion solvent-free floor covering adhesive with a high initial grab.
Eurocol 640 Eurostar Special – A superior acrylic dispersion low VOC emission adhesive with a high initial grab.
Eurocol 140 Euromix PU – A polyurethane resin and hardener, water-resistant 2-component PU-adhesive.                                                                                                                                                                 Eurocol 233 Eurosol Contact – A synthetic rubber in solvent fast setting contact adhesive.

Seam welding: Joints to be cold welded with Forbo Noviweld 671

Accessories:
Edging and cover strips, as clause 740.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polished finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.