To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

Allura Flex 0.55 is a range of high quality, dimensionally stable, heterogeneous vinyl tiles that have been specifically designed for loose lay installation.

The subtle designs complement all types of spaces, providing a tough, resilient flooring surface suitable for the most demanding of situations.

Dimensions: 50 x 50cm; 75 x 50 cm;100 x 20cm; 120 x 20cm; 150 x 28cm and 80 x 80cm*.
Thickness: 4 mm (0.55mm wear layer);

Colours/ patterns: 35 standard designs/colourways
Edge Profile: Bevelled or Square*

Finish - in register embossing*

* Dependent on colourway/design

Consult with Forbo technical literature for details.

110 TILING: VINYL.

Fabricated underlay: 
Forbo QuickFit Subfloor System. – Optional.

Tiles: Vinyl to EN651

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley DE5 3NT

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Allura Flex 0.55

BS EN ISO 10874 class: 33 / 42

Size: 50 x 50cm; 75 x 50 cm; 100 x 20cm; 120 x 20cm, 150 x 28cm. 80 x 80cm [dependant on Colour/Pattern].

Thickness: 4 mm

Colour/ pattern: Key: b = beveled edges

50 cm x 50 cm; 	1947 b,1941 b,1944 b,1953,1954,1955,1957

75cm x50cm: 		1967,1968,1969,1956,1958

100 x 20cm: 		1991b, 1992 b, 1993 b, 1994b, 1995b, 1996 b, 1997 b, 1998 b, 1999 b, 1984 b, 				1987b,1985b,1986 b,1988 b

120 x 20cm: 		1972,1973,1974,1975,1976,1977,

150 x 28cm: 		1911 b,1912 b,1913 b,1914 b,1915 b

80 x 80cm:		1948,1942,1945

Adhesive (and primer if recommended by manufacturer): 542 Eurofix Tack Plus.

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.