To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Marmoleum® Linear - Striato Textura. A range of linoleum floor coverings with a linear design structure and embossed surface structure, which is part of the Marmoleum® linear collection. The collection offers 2 different types of surface embossing: Flow and Driftwood. They both are linear textures, following the Striato design. Flow has depth and is more appealing from a distance, the grayish palette is used for this design. Driftwood is a subtle linear design and enhances the naturalness of the stripe and the warm colours.

Roll width: 2000 mm.
Thickness: 2.5 mm.

Colours: 7 standard colours (4 colours with Driftwood embossing: 3 colours with Flow embossing)

Please note that Striato Textura should be installed with net-fit seams and not welded.

Consult with Forbo technical literature for details.

150 SHEETING: LINOLEUM

Fabricated underlay: [select for the list below if needed]
Forbo Corkment Underlay. – Optional.
Forbo QuickFit Subfloor System. – Optional.
Forbo Sarlibase T.E. Underlay. – Optional.

Flooring roll: Linoleum to BS EN ISO 24011.
Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, Derbyshire DE5 3NT

Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com

Web: www.forbo-flooring.co.uk

Product reference: Forbo Marmoleum® Linear - Striato Textura

BS EN 685 class: 23 / 34 / 43.

Width: 2000 mm

Thickness: 2.5 mm

Colour/ pattern: select as required from; E3573/E5216/E5217/E5231/E5232/E5235/E5236

Adhesive (and primer if recommended by manufacturer):
Eurocol 414/696 Euroflex Lino Plus – A synthetic resin dispersion adhesive with a high initial grab.
Eurocol 614 Eurostar Lino Plus – A superior acrylic dispersion very low VOC-emission adhesive with a high initial grab – to be specified where low emission adhesives are required for BREEAM section HEA9 credits are required

Seam welding: Not required

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820, omitting polish finish

Other requirements: 
Seek advice from Forbo for specific requirements for flooring.

460 SMOOTHING/LEVELLING UNDERLAYMENT COMPOUND

Forbo Flooring in association with Forbo Bonding Systems (Forbo Eurocol) manufacture a range of smoothing underlayment compounds:

Forbo Eurocol 902 Europlan Latex Premium; Forbo Eurocol 920 Europlan Alphy

Forbo Eurocol 902 Europlan Latex Premium
A cement based powder/latex mix smoothing compound. 902 Europlan Latex Premium can be used to prepare and smooth uneven internal subfloors such as power floated concrete, tamped or pan floated concrete, sand cement screeds, stone, flooring grade asphalt (min. 3mm and max. 6mm), plywood, non-flexing steel decks (mezzanine decks), thin, firmly bonded adhesive residues (min.3 mm), surface DPM’s, terrazzo granolithic, porcelain and ceramic tiles. For use in domestic, light commercial and industrial environments as a smoothing underlayment, prior to the application of resilient type floor finishes.

Although 902 Europlan Latex Premium can be used as a self-priming system, both porous and nonporous substrates are best primed, as this will help to increase inter bond adhesion and reduce the possibility of debonding issues occurring. When deemed a requirement, prime the base with 044 Europrimer Multi. See clause M50/10 and 20 ‘Preparation’ for details.

Consult Forbo Eurocol technical literature for details.

Type: Latex/Powder mix

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, Derbyshire DE5 3NT

Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com

Web: www.forbo-flooring.co.uk

Product reference: Forbo Eurocol 902 Europlan Latex Premium

Application: Trowel or toothed smoothing trowel applied – minimum thickness 3mm. Protect fresh layers against draughts and direct sunlight.
When applying to an underfloor heated subfloor, the heating is to be turned off 24 hours before application and heat is not to be applied for at least 24 hours after application, in steps of 5°C per day.

Forbo Eurocol 920 Europlan Alphy
A self-smoothing, tension-free hardening levelling compound particularly suitable for anhydrite subfloors and designed for levelling in layers between 0.5 and 30mm thickness.

Smooth and impervious subfloors (ceramic, granolithic, terrazzo), asphalt and bituminous floors to be primed with 044 Europrimer Multi. Highly absorbent subfloors to be primed with 044 Europrimer Multi. See clause M50/10 and 20 ‘Preparation’ for details.

Consult Forbo Eurocol technical literature for details.

Type: Water/powder mix

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, Derbyshire DE5 3NT

Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com

Web: www.forbo-flooring.co.uk

Product reference: Forbo Eurocol 920 Europlan Alphy

Application: Trowel or toothed smoothing trowel. Protect fresh layers against draughts and direct sunlight.
When applying to an underfloor heated subfloor, the heating is to be turned off 24 hours before application and heat is not to be applied for at least 24 hours after application, in steps of 5°C per day.