To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Marmoleum® Linear - Striato Colour. A range of linoleum floor coverings with a linear design structure, which is part of the Marmoleum® linear collection. The colour palette comprises four rich colour tones alongside four softer neutral colour tones which can be used on their own, or to compliment other colours in the Marmoleum Colour range.

Roll width: 2000 mm.
Thickness: 2.5 mm.

Colours: 8 standard colours

Matching welding rods are available in all collection colours.

Consult with Forbo technical literature for details.

150 SHEETING: LINOLEUM

Fabricated underlay: [select for the list below if needed]
Forbo Corkment Underlay. – Optional.
Forbo QuickFit Subfloor System. – Optional.
Forbo Sarlibase T.E. Underlay. – Optional.

Flooring roll: Linoleum to BS EN ISO 24011.
Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, Derbyshire DE5 3NT

Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com

Web: www.forbo-flooring.co.uk

Product reference: Forbo Marmoleum® Linear - Striato Colour

BS EN 685 class: 23 / 34 / 43.

Width: 2000 mm

Thickness: 2.5 mm

Colour/ pattern: select as required from; 5221/5241/5242/5243/5244/5245/5246/5247

Adhesive (and primer if recommended by manufacturer):
Eurocol 414/696 Euroflex Lino Plus – A synthetic resin dispersion adhesive with a high initial grab.
Eurocol 614 Eurostar Lino Plus – A superior acrylic dispersion very low VOC-emission adhesive with a high initial grab – to be specified where low emission adhesives are required for BREEAM section HEA9 credits are required

Seam welding: Not required / hot welded with Marmoweld weld rod (delete as appropriate).

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820, omitting polish finish

Other requirements: 
Seek advice from Forbo for specific requirements for flooring.

# 770 Skirtings

# Type: Set in Skirting

Manufacturer and reference: Marmoform S / Marmoform SW Coving by Forbo Flooring UK Ltd.

Size: 100 mm high x 50 mm toe.

Thickness: 2.5 mm

Colour/pattern: _________

Adhesive (and primer if recommended by manufacturer): Contact adhesive.

Securely bond with top edge straight and parallel with floor. Accurately mitre at corners except where pre-formed angles are used. All mitred and horizontal joints to be hot seam welded using matching Marmoweld weld cable (except where pre-formed angles are used). Vertical joints may be either hot seam welded or sealed with clear silicone sealant applied to the exposed edge of each section of skirting prior to sticking the next section of coving – contact Forbo Nairn for further details if required.

# Type: Flat Skirting

Manufacturer and reference: Marmostrip SW Flat skirting strip by Forbo Flooring UK Ltd.

Size: 55 mm high.

Thickness: 2.5 mm

Colour/pattern: _________

Adhesive (and primer if recommended by manufacturer): Contact adhesive.

Securely bond with top edge straight and parallel with floor. Accurately mitre at corners. All mitred joints to be hot seam welded using matching Marmoweld weld cable. Vertical joints may be either hot seam welded or sealed with clear silicone sealant applied to the exposed edge of each section of skirting prior to sticking the next section of coving – contact Forbo Nairn for further details if required.

Type: Self coved skirting

Cove former: Quantum Profile Systems reference QCF35 - 35mm radius tapered to architraves. Securely bond to base and background using contact adhesive. Accurately mitre at corners.

Capping strip: Quantum Profile Systems UCS2 PVC capping strip.

Securely bond to background using contact adhesive, with top edge straight and parallel with floor.

Turn flooring material up wall, securely bond to cove former and background using adhesive specified for fixing to base, and ease top of material into edge trim. Accurately mitre at corners. All joints to be hot welded in accordance with the manufacturer’s instructions.

Height: [insert required height] mm

460 SMOOTHING/LEVELLING UNDERLAYMENT COMPOUND

Forbo Flooring in association with Forbo Bonding Systems (Forbo Eurocol) manufacture a range of smoothing underlayment compounds.

Forbo Eurocol 902 Europlan Latex Premium
Forbo Eurocol 920 Europlan Alphy

Forbo Eurocol 902 Europlan Latex Premium
A cement based powder/latex mix smoothing compound. 902 Europlan Latex Premium can be used to prepare and smooth uneven internal subfloors such as power floated concrete, tamped or pan floated concrete, sand cement screeds, stone, flooring grade asphalt (min. 3mm and max. 6mm), plywood, non-flexing steel decks (mezzanine decks), thin, firmly bonded adhesive residues (min.3 mm), surface DPM’s, terrazzo granolithic, porcelain and ceramic tiles. For use in domestic, light commercial and industrial environments as a smoothing underlayment, prior to the application of resilient type floor finishes.

Although 902 Europlan Latex Premium can be used as a self-priming system, both porous and nonporous substrates are best primed, as this will help to increase inter bond adhesion and reduce the possibility of debonding issues occurring. When deemed a requirement, prime the base with 044 Europrimer Multi. See clause M50/10 and 20 ‘Preparation’ for details.

Consult Forbo Eurocol technical literature for details.

Type: Latex/Powder mix

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, Derbyshire DE5 3NT

Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com

Web: www.forbo-flooring.co.uk

Product reference: Forbo Eurocol 902 Europlan Latex Premium

Application: Trowel or toothed smoothing trowel applied – minimum thickness 3mm. Protect fresh layers against draughts and direct sunlight.
When applying to an underfloor heated subfloor, the heating is to be turned off 24 hours before application and heat is not to be applied for at least 24 hours after application, in steps of 5°C per day.

Forbo Eurocol 920 Europlan Alphy
A self-smoothing, tension-free hardening levelling compound particularly suitable for anhydrite subfloors and designed for levelling in layers between 0.5 and 30mm thickness.
Smooth and impervious subfloors (ceramic, granolithic, terrazzo), asphalt and bituminous floors to be primed with 044 Europrimer Multi. Highly absorbent subfloors to be primed with 044 Europrimer Multi. See clause M50/10 and 20 ‘Preparation’ for details.
Consult Forbo Eurocol technical literature for details.

Type: Water/powder mix

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, Derbyshire DE5 3NT

Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com

Web: www.forbo-flooring.co.uk

Product reference: Forbo Eurocol 920 Europlan Alphy

Application: Trowel or toothed smoothing trowel. Protect fresh layers against draughts and direct sunlight.
When applying to an underfloor heated subfloor, the heating is to be turned off 24 hours before application and heat is not to be applied for at least 24 hours after application, in steps of 5°C per day.