To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

Allura Click is a range of 38 wood and stone designs that offer exceptional dimensional stability. Featuring the patented locking system from Unilin, Allura Click will retain its appearance over time with no gaps or seams appearing.

Dimensions: 60 x 31.7cm; 121.2 x 18.7cm; 150.5 x 23.7cm.*.
Thickness: 5 mm (0.55mm wear layer);

Colours/ patterns: 38 standard designs/colourways.
Edge Profile: Bevelled or Square*

* Dependent on colourway/design

Consult with Forbo technical literature for details.

110 TILING: VINYL.

Fabricated underlay: 
Allura Click Underlay. – Optional.

Tiles: Vinyl to BS EN ISO 10582

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, DE5

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Allura Click.

BS EN ISO 10874 class: 33

Size: 60 x 31.7cm; 121.2 x 18.7cm; 150.5 x 23.7cm [delete as appropriate].

Thickness: 5 mm

Colour/ pattern: Key: b = beveled

60 x 31.7cm: cc62418/cc62523/cc62522/cc62419/cc62404/cc62488/cc62485/cc63604/cc63776

121.2 x 18.7cm: cc60005(b)/cc60026/cc60065/cc60064/cc60078(b)/cc60074(b)/cc60373(b)/cc60374(b)/cc60375(b)/cc60376(b)/cc60295(b)/cc60293(b)/cc60085(b)/cc60082(b)/cc60084(b)/cc66350(b)/cc60353(b)/cc60356(b)/cc61255(b)/cc61241(b)/cc60664(b)

150.5 x 23.7cm: cc60305(b)/cc60300(b)/cc60302(b)/cc60306(b)/cc60280(b)/cc60282(b)/cc60284(b)/cc60286(b)

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.