To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

130 CARPET TILE:

Flotex Planks:   An electrostatic flocked carpet tile manufactured from 100% nylon 6.6 pile with a resilient waterproof backing.

Tile Size: 100cm x 25cm 							                               Thickness: 5.0mm

Flotex Planks are available in the following patterns ranges/colourways: (Triad 15 colours & 1 embossed) / Box-cross (9 colours) / Seagrass (6 colours) / Concrete (8 colours) / Wood (8 colours) / Marble (4 colours) / Ombre (8 colours) / Montage (8 colours) / Converge (7 colours) / Frameweave (16 colours) / Refract (6 colours)

Consult with Forbo technical literature for further details.

130 CARPET TILE:

Manufacturer: Forbo Flooring Systems Ltd, High Holborn Road, Ripley, Derbyshire, DE5 3NT.  Tel: 0800 0282 162 Fax: 01772 646912.  Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Flotex Planks– Select from the following ranges:

Triad / Box-cross / Seagrass / Concrete / Wood / Marble / Ombre / Montage / Converge / Frameweave / Refract

Type: Flocked Carpet Plank

BS EN 685 classification: Class 33

Level of use class: Heavy Contract

Size: 1000 x 250 mm

Colour/ pattern: As per finishes schedule

Adhesive (and primer if recommended by manufacturer):

542 Eurofix Tack Plus – Low emission* high grab tackifier

640 Eurostar Special – A superior acrylic dispersion low VOC emission* adhesive with a high initial grab - specify where a permanent bond is required – see manufacturers installation guide.

*Specify where BREEAM section HEA2 or HEA9 credits are required.

Method of Laying: Flotex carpet planks must be laid in accordance with best practice techniques as detailed in the Contract Flooring Association’s guidelines and BS5325.  For additional information consult manufacturer’s fitting instructions or contact Forbo Flooring UK Ltd.

Consult with Forbo technical literature for laying methods per design.

### Accessories:
Edging and cover strips, as clause 740.

Other requirements:  Flotex Planks has the Allergy UK Seal of approval