To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

130 CARPET TILE:

Tessera Layout and Outline carpet tile planks:   A tufted, low loop pile carpet tile. Manufactured with 100% solution dyed nylon 6 on a polyester/nylon primary backing and a modified bitumen/polyester secondary backing. The collection consists of a solid ‘Layout’ palette with complementary striped ‘Outline’ colours. All plank colours are also available in a 50x50cm tile version.

Tile size: 100 x 25cm

Pile weight: 580g/sm ± 10%

Thickness: 5.8mm ± 10%

Colours/patterns: Layout – 14 colours & Outline – 4 colours

Layout and Outline contains 63% recycled content by weight.

Tessera carpet tiles must be laid in accordance with best practice techniques as detailed in the Contract Flooring Association’s guidelines and BS5325.  Consult with Forbo technical literature for further details.

130 CARPET TILE:

Manufacturer: Forbo Flooring Systems Ltd, High Holborn Road, Ripley, Derbyshire, DE5 3NT.  Tel: 0800 0282 162 Fax: 01772 646912.  Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Layout and Outline Planks

Type: Low loop pile

BS EN 1307 classification: Class 33

Level of use class: Heavy Contract

Size: 100 x 25 cm

Colour/ pattern: As per finishes schedule

Method of Laying:

Layout: Brick, herringbone, double herringbone, half-drop, weave or monolithic [delete as appropriate].

Outline: Brick, herringbone, double herringbone, half-drop or weave [delete as appropriate].

Adhesive: 542 Eurofix Tack Plus.

Accessories: Edging and cover strips, as clause 740.