To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

N10 GENERAL FIXTURES/ FURNISHINGS/ EQUIPMENT

300 ENTRANCE MATTING:

Coral Click is an exceptionally versatile ‘off the shelf’ modular matting system that can be assembled on site.

Coral Click can be used on its own or in conjunction with our Coral textile ranges to provide an integrated entrance system. This versatile PVC tile with Coral textile inserts can be used in all types of buildings and, because it contains no metal components, Coral click entrance floors are particularly suitable for installation in the retail environment as it does not interfere with electronic-tagging systems.

Coral Click is also available without textile inserts (plain) for bordering/framing of the main field in 12mm & 17mm thicknesses.

Textile: Coral Brush, constructed from 100% Econyl® regenerated solution dyed polyamide yarn

Backing: Injection moulded UV resistant PVC

Tile size: 24 x 24 cm

Overall thickness:

12mm textile – 14mm

17mm textile – 19mm

12mm plain – 11mm

17mm textile – 16mm

Colour/pattern:

12mm – 7830 / 7831 / 7833 / 7834 / 7837 / 7838 / plain

17mm – 7880 / 7881 / 7883 / 7884 / 7887 / 7888 / plain

300 ENTRANCE MATTING:

Manufacturer:

Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Coral Click

Size: 24 x 24 cm

Colour/ pattern: Select from the following:

12mm – 7830 / 7831 / 7833 / 7834 / 7837 / 7838 / plain

17mm – 7880 / 7881 / 7883 / 7884 / 7887 / 7888 / plain

Matwell Frame: Select from the following options:

Existing

Recessed Aluminium AMF253/AMF346/AMF506

Ramped Aluminium: 12mm ARF 50 / 17mm ARF 70

Method of Laying: Monolithic/Tessellated – other laying option are available – see manufacturer’s installation guidance