To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Fabscrap: A range of homogeneous project vinyl coverings, with SMARTOP PUR surface finish offering ease of maintenance and a long-lasting sheen.

Created using the left-over chips from Forbo’s Sphera homogeneous production process, Fabscrap has a recognizable non directional homogeneous vinyl visual. Using a chip mix of 7 to 8 bright colours against a neutral base tone taken from the Sphera Element colour palette, the resulting visual resembles a colourful terrazzo.

4 colours are available as stock items: F50000 white, F50004 mid neutral grey, F50018 mortar, F50037 china blue.

Bespoke options are available and are subject to minimum order quantities. Information and lead time on request.

Roll width: 2000 mm.   Thickness: 2.0 mm.
Colours/ patterns: 4 colourways

Unicolour welding rods to match the base colour are available.

Consult with Forbo technical literature for details.

150 SHEETING: VINYL

Fabricated underlay (delete where not required)

Forbo QuickFit Subfloor System. – Optional.
Forbo Vinylbase acoustic underlay – Optional

Flooring roll: Homogeneous PVC to BS EN ISO 10581

Manufacturer: Forbo Flooring Systems Ltd, High Holborn Road, Ripley, Derbyshire, DE5 3NT.  Tel: 0800 0282 162 Fax: 01772 646912.  Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Fabscrap

BS EN 685 class: 34 / 42.
Width: 2000 mm
Thickness: 2.0 mm
Colour/ pattern: As finishes schedule

Adhesive (and primer if recommended by manufacturer):
Eurocol 540 Eurosafe Special – A superior acrylic dispersion solvent-free floor covering adhesive with a high initial grab.
Eurocol 640 Eurostar Special – A superior acrylic dispersion low VOC emission adhesive with a high initial grab.
Eurocol 140 Euromix PU – A polyurethane resin and hardener, water-resistant 2-component PU-adhesive.

Seam welding: Hot welding with matching coloured rod.

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polished finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.

770 Skirting

Type: Self coved skirting

Cove former: ECF4 35mm radius by Quantum Profiles tapered to architraves. Securely bond to base and background using contact adhesive. Accurately mitre at corners.

Top edge trim: UCS2 PVC capping strip by Quantum profiles. Securely bond to background using contact adhesive, with top edge straight and parallel with floor.

Turn flooring material up wall, securely bond to cove former and background using adhesive specified for fixing to base, and ease top of material into edge trim. Accurately mitre at corners. All joints to be hot welded in accordance with the manufacturer’s instructions.

Height: ______