To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Marmoleum® Marbled. A range of linoleum floor coverings offering 90 colourways and five design structures, Real, Fresco, Vivace, Terra and Splash. All 2.5mm sheet Marmoleum is produced CO₂ neutral from cradle-to-gate.

Roll width: 2000 mm.

Thickness: all colours 2.5mm. Some colours are available in 2.0mm and 3.2 mm.

Matching welding rods are available in all collection colours.

Seam welding is not essential for the successful installation of Marmoleum and where the usage application allows an enhanced seamless visual is offered using unwelded net fit seams.

Where the application requires seam welding matching welding rods are available in all collection colours:

Multi-coloured welding rods are available for all colourways in Vivace, Terra and Splash ranges to create invisible or decorative seams.

Weld rod options for Real and Fresco colourways are either Uni colour or Multi coloured depending on the colourway.

Consult with Forbo technical literature for details

150 SHEETING: LINOLEUM

Fabricated underlay: 
Forbo Corkment Underlay. – Optional.
Forbo QuickFit Subfloor System. – Optional.
Forbo Sarlibase T.E. Underlay. – Optional.

Flooring roll: Linoleum to BS EN ISO 24011.
Manufacturer: Forbo Flooring UK Ltd, PO Box 1, Kirkcaldy, Fife KY1 2SB Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com Web: www.forbo-flooring.co.uk

Product reference: Forbo Marmoleum® Marbled Real /Fresco /Vivace/Terra/Splash

BS EN 685 class:
23 / 32 / 41. – for 2.0 mm.
23 / 34 / 42. – for 2.5 and 3.2 mm.

Width: 2000 mm

Thickness: 2.0 mm / 2.5 mm / 3.2 mm (select gauge according to availability in within chosen range)

Colour/ pattern: As per finishes schedule

Adhesive (and primer if recommended by manufacturer):
Eurocol 414/696 Euroflex Lino Plus – A synthetic resin dispersion adhesive with a high initial grab.
Eurocol 614 Eurostar Lino Plus – A superior acrylic dispersion very low VOC-emission adhesive with a high initial grab – to be specified where low emission adhesives are required for BREEAM section HEA9 credits are required

Seam welding: Not required / Hot welded with Marmoweld weld rod (delete as appropriate).

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820, omitting polish finish

Other requirements: 
Seek advice from Forbo for specific requirements for flooring.

# 770 Skirtings

# Type: Set in Skirting

Manufacturer and reference: Marmoform S / Marmoform SW Coving by Forbo-Nairn Ltd.

Size: 100 mm high x 50 mm toe.

Thickness: 2.5 mm

Colour/pattern: _________

Adhesive (and primer if recommended by manufacturer): Contact adhesive.

Securely bond with top edge straight and parallel with floor. Accurately mitre at corners except where pre-formed angles are used. All mitred and horizontal joints to be hot seam welded using matching Marmoweld weld cable (except where pre-formed angles are used). Vertical joints may be either hot seam welded or sealed with clear silicone sealant applied to the exposed edge of each section of skirting prior to sticking the next section of coving – contact Forbo Nairn for further details if required.

# Type: Flat Skirting

Manufacturer and reference: Marmostrip SW Flat skirting strip by Forbo-Nairn Ltd.

Size: 55 mm high.

Thickness: 2.5 mm

Colour/pattern: _________

Adhesive (and primer if recommended by manufacturer): Contact adhesive.

Securely bond with top edge straight and parallel with floor. Accurately mitre at corners. All mitred joints to be hot seam welded using matching Marmoweld weld cable. Vertical joints may be either hot seam welded or sealed with clear silicone sealant applied to the exposed edge of each section of skirting prior to sticking the next section of coving – contact Forbo Nairn for further details if required.

Type: Self coved skirting

Cove former: Quantum Profile Systems reference QCF35 - 35mm radius tapered to architraves. Securely bond to base and background using contact adhesive. Accurately mitre at corners.

Capping strip: Quantum Profile Systems UCS2 PVC capping strip.

Securely bond to background using contact adhesive, with top edge straight and parallel with floor.

Turn flooring material up wall, securely bond to cove former and background using adhesive specified for fixing to base, and ease top of material into edge trim. Accurately mitre at corners. All joints to be hot welded in accordance with the manufacturer’s instructions.

Height: [insert required height] mm