To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

130 CARPET TILE:

Tessera Chroma: A tufted textured loop pile carpet tile. Manufactured with 100% solution dyed polyamide 6, on polyester primary and a modified bitumen and polyester secondary backing.

Tile size: 50 x 50cm, other sizes are available for special orders.

Pile weight: 750g/sm ± 10%

Thickness: 6.4mm ± 10%

Chroma is available in 27 colourways.

Tessera carpet tiles must be laid in accordance with best practice techniques as detailed in the Contract Flooring Association’s guidelines and BS5325. Consult with Forbo technical literature for further details.

130 CARPET TILE:

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, Derbyshire, DE5 3NT.

Tel: 01773 744 121 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Tessera Chroma

Type: Tufted textured loop pile carpet tile

BS EN 1307 classification: Class 33

Level of use class: Heavy Contract

Size: 50 x 50cm

Colour/ pattern: [select from] 3600/3601/3602/3603/3604/3605/3606/3607/3608/3609/3610/3611/3612/3613/3614/3615/3616/3617/3618/3619/3620/3621/3622/3623/3624/3625/3626

Method of Laying: Monolithic, quarter turn or tessellated

Adhesive: 542 Eurofix Tack Plus

Accessories: Edging and cover strips, as clause 740.