To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

170 Carpet: . . . . . .

An electrostatically Flocked carpet manufactured from 100% nylon 6.6 pile with a Resilient Waterproof backing. With Flotex Artline you are able to make borders, creative features and delineators between colour ways or even different designs.

Flotex Artline is available in two widths and matches the base shades of the various Flotex Colour and Linear designs.

Roll width; 110mm and 220mm

Thickness: 4.3mm

Flotex Artline is available in 26 plain colours

Consult with Forbo technical literature for details.

170 Carpet:

Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Flotex Artline

Roll width: 110mm

220mm

(delete as appropriate)

BS EN 685 classification: Class 33

Level of use class: Heavy Contract

Colour/ pattern: As per finishes schedule

Adhesive (and primer if recommended by manufacturer):
Eurocol 540 Eurosafe Special – A superior acrylic dispersion solvent-free floor covering adhesive with a high initial grab.
Eurocol 640 Eurostar Special – A superior acrylic dispersion low VOC emission adhesive with a high initial grab.

Other requirements: 
Seek advice from Forbo for specific requirements for flooring.