To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

130 CARPET TILE:

Flotex Tile:   An electrostatic flocked carpet tile manufactured from 100% nylon 6.6 pile with a resilient waterproof backing.

Tile Size: 50cm x 50cm 							                               Thickness: 5.3mm

Flotex Linear Tile is available in the following patterns ranges/colourways: Stratus (15 colourways); Cirrus (10 colourways); Pinstripe (12 colourways); Intergrity2 (12 colourways); Complexity (10 colourways)

Consult with Forbo technical literature for further details.

130 CARPET TILE:

Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Flotex Linear Tile– Select from the following ranges:

Stratus/Cirrus/Pinstripe/Integrity2/Complexity

Type: Flocked Carpet Tile

BS EN 685 classification: Class 33

Level of use class: Heavy Contract

Size: 500 x 500mm

Colour/ pattern: As per finishes schedule

Adhesive (and primer if recommended by manufacturer):

542 Eurofix Tack Plus – Low emission* high grab tackifier

Eurocol 540 Eurosafe Special – A superior acrylic dispersion solvent-free floor covering adhesive with a high initial grab - specify where a permanent bond is required – see manufacturers installation guide.
Eurocol 640 Eurostar Special – A superior acrylic dispersion low VOC emission* adhesive with a high initial grab - specify where a permanent bond is required – see manufacturers installation guide.

*Specify where BREEAM section HEA2 or HEA9 credits are required.

Method of Laying: Flotex carpet tiles must be laid in accordance with best practice techniques as detailed in the Contract Flooring Association’s guidelines and BS5325.  For additional information consult manufacturer’s fitting instructions or contact Forbo Flooring UK Ltd.

Laying Options:

Stratus and Cirrus: [select from] Broadloom; Tessellated; Brick bond; Half drop.

Pinstripe: [Select from] Tessellated; Brick bond; Half drop.

Integrity2: Tessellated

Complexity: [Select from] Tessellated; Brick bond:

### Accessories:
Edging and cover strips, as clause 740.

Other requirements:  Flotex Linear Tile has the Allergy UK Seal of approval