To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Marmoleum® Decibel. Part of the Marmoleum Marbled collection, Marmoleum Decibel is suitable for residential and commercial applications where additional acoustic properties are required. Marmoleum® Decibel provides a weighted impact sound reduction of 18dB. Suitable for office chairs with castors.

Roll width: 2000 mm. Thickness: 3.5 mm.

Standard colours: 14

Matching welding rods are available in all collection colours. Moreover, the multi-coloured welding rods can be used to create invisible or decorative seams.

Consult with Forbo technical literature for details.

150 SHEETING: LINOLEUM

Flooring roll: Linoleum to BS EN 686.
Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Marmoleum® Decibel – 3.5mm thick

BS EN 685 class: 23 / 33 / 41                                                                                                                                                          Width: 2000 mm
Thickness: 3.5mm                                                                                                                                           Colour/ pattern: As per finishes schedule

Adhesive (and primer if recommended by manufacturer):
Eurocol 540 Eurosafe Special – A superior acrylic dispersion solvent-free floor covering adhesive with a high initial grab.                                                                                                                                Eurocol 640 Eurostar Special – A superior acrylic dispersion very low VOC emission adhesive with a high initial grab – to be specified where low emission adhesives are required for BREEAM section HEA9 credits are required

Seam welding: Hot welding with matching coloured rod.

Accessories:
Edging / cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820, omitting polish finish

Other requirements: 
Seek advice from Forbo for specific requirements for flooring.