To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Marmoleum®. A range of marble effect and plain linoleum floor coverings, which are part of the Next Generation of Marmoleum® range, which includes Real, Vivace, Fresco, Graphic, Piano, Walton, Concrete, Striato, Ohmex, Acoustic, Decibel and Marmoleum® meets Mendini.
Roll width: 2000 mm.
Thickness: 2.0 mm; 2.5 mm. Some colours are available in 3.2 mm and 4.0 mm.
Matching welding rods are available in all collection colours. Moreover, the multi-coloured welding rods can be used to create invisible or decorative seams. GloWeld – A photo luminescent welding rod that can be applied for functional reasons, such as safety markings, so that people can find their way in the dark.
Consult with Forbo technical literature for details.

150 SHEETING: LINOLEUM

Fabricated underlay: 
Forbo Corkment Underlay. – Optional.
Forbo QuickFit Subfloor System. – Optional.
Forbo Sarlibase T.E. Underlay. – Optional.

Flooring roll: Linoleum to BS EN 548.
Manufacturer: Forbo Flooring UK Ltd, PO Box 1, Kirkcaldy, Fife KY1 2SB Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com Web: www.forbo-flooring.co.uk  
Product reference: Forbo Marmoleum® Select from the following ranges:

Real /Fresco /Vivace /Graphic /Piano /Walton Uni / Walton Cirrus /Concrete /Striato

BS EN 685 class:
23 / 32 / 41. – for 2.0 mm.
23 / 34 / 42. – for 2.5 and 3.2 mm.
23 / 34 / 43. – for 4.0 mm.
Width: 2000 mm
Thickness: 2.0 mm / 2.5 mm / 3.2 mm / 4.0 mm (select gauge according to availability in within chosen range)                                                                                                                                                      Colour/ pattern: As per finishes schedule

Adhesive (and primer if recommended by manufacturer):
Eurocol 414/696 Euroflex Lino Plus – A synthetic resin dispersion adhesive with a high initial grab.
Eurocol 614 Eurostar Lino Plus – A superior acrylic dispersion very low VOC-emission adhesive with a high initial grab.
Eurocol 233 Eurosol Contact – A synthetic rubber in solvent fast setting contact adhesive.

Seam welding: Not required / Hot welded with Marmoweld weld rod (delete as appropriate).

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820, omitting polish finish

Other requirements: 
Seek advice from Forbo for specific requirements for flooring.

# 770 Skirtings

# Type: Set in Skirting

Manufacturer and reference: Marmoform S / Marmoform SW Coving by Forbo-Nairn Ltd.

Size: 100 mm high x 50 mm toe.

Thickness: 2.5 mm

Colour/pattern: _________

Adhesive (and primer if recommended by manufacturer): Contact adhesive.

Securely bond with top edge straight and parallel with floor. Accurately mitre at corners except where pre-formed angles are used. All mitred and horizontal joints to be hot seam welded using matching Marmoweld weld cable (except where pre-formed angles are used). Vertical joints may be either hot seam welded or sealed with clear silicone sealant applied to the exposed edge of each section of skirting prior to sticking the next section of coving – contact Forbo Nairn for further details if required.

# Type: Flat Skirting

Manufacturer and reference: Marmostrip SW Flat skirting strip by Forbo-Nairn Ltd.

Size: 55 mm high.

Thickness: 2.5 mm

Colour/pattern: _________

Adhesive (and primer if recommended by manufacturer): Contact adhesive.

Securely bond with top edge straight and parallel with floor. Accurately mitre at corners. All mitred joints to be hot seam welded using matching Marmoweld weld cable. Vertical joints may be either hot seam welded or sealed with clear silicone sealant applied to the exposed edge of each section of skirting prior to sticking the next section of coving – contact Forbo Nairn for further details if required.

Type: Self coved skirting

Cove former: 38mmradius tapered to architraves. Securely bond to base and background using contact adhesive. Accurately mitre at corners.

Top edge trim: HCS48 PVC capping strip to all other areas. Securely bond to background using contact adhesive, with top edge straight and parallel with floor.

Turn flooring material up wall, securely bond to cove former and background using adhesive specified for fixing to base, and ease top of material into edge trim. Accurately mitre at corners. All joints to be hot welded in accordance with the manufacturer’s instructions.

Height: ______

460 SMOOTHING/LEVELLING UNDERLAYMENT COMPOUND

Forbo Flooring in association with Eurocol manufacture a range of smoothing underlayment compounds. 
Forbo Eurocol 920 Europlan Alphy
Forbo Eurocol 975 Europlan Special
Forbo Eurocol 990 Europlan Direct

Forbo Eurocol 920 Europlan Alphy
A self-smoothing, tension-free hardening leveling compound for stony subfloors and especially for anhydrite subfloors and designed for leveling in layers between 0.5 and 30mm thickness.
Smooth and impervious subfloors (ceramic, granolithic, terrazzo), asphalt and bituminous floors to be primed with 044 Europrimer Multi. Highly absorbent subfloors to be primed with 044 Europrimer Multi or 049 Europrimer ABS. See clause M50/10 and 20 ‘Preparation’ for details.
Consult Forbo Flooring Ltd’s technical literature for details.

Type: Water/powder mix 
Manufacturer: Forbo Flooring UK Ltd, PO Box 1, Kirkcaldy, Fife KY1 2SB 
Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com Web: www.forbo-flooring.co.uk  
Product reference: Forbo Eurocol 920 Europlan Alphy
Application: Trowel or toothed smoothing trowel. Protect fresh layers against draughts and direct sunlight.
Where applying to an underfloor heated subfloor, the heating is to be turned off 24 hours before application and heat is not to be applied for at least 24 hours after application, in steps of 5°C per day.


Forbo Eurocol 975 Europlan Special
A self-smoothing leveling compound for stony subfloors and designed for leveling in layers up to 8mm thickness.
Smooth and impervious subfloors (ceramic, granolithic, terrazzo), asphalt and bituminous floors to be primed with 044 Europrimer Multi. Highly absorbent subfloors to be primed with 044 Europrimer Multi or 049 Europrimer ABS. See clause M50/10 and 20 ‘Preparation’ for details.
Consult Forbo Flooring Ltd’s technical literature for details.

Type: Water/Powder mix
Manufacturer: Forbo Flooring UK Ltd, PO Box 1, Kirkcaldy, Fife KY1 2SB 
Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com Web: www.forbo-flooring.co.uk  
Product reference: Forbo Eurocol 975 Europlan Special
Application: Trowel or toothed smoothing trowel applied. 
Where applying to an underfloor heated subfloor, the heating is to be turned off 24 hours before application and heat is not to be applied for at least 24 hours after application, in steps of 5°C per day.

Forbo Eurocol 990 Europlan Direct
A self-smoothing very high quality leveling compound especially suitable for critical for stony subfloors and designed for leveling in layers up to 20mm thickness.
Smooth and impervious subfloors (ceramic, granolithic, terrazzo) to be degreased with 014 Euroclean and rinsed with water. They do not normally require to be primed. Porous subfloors do not require to be primed but highly absorbent subfloors to be primed with 044 Europrimer Multi. Highly absorbent subfloors to be primed with 044 Europrimer Multi or 049 Europrimer ABS. See clause M50/10 and 20 ‘Preparation’ for details.
Consult with Forbo Flooring Ltd if applying to asphalt and bituminous floors.
Consult Forbo Flooring Ltd’s technical literature for details.

Type: Water/Powder mix
Manufacturer: Forbo Flooring UK Ltd, PO Box 1, Kirkcaldy, Fife KY1 2SB 
Tel: 0800 0282 162 Fax: 01772 646 912 E-mail: info.flooring.uk@forbo.com Web: www.forbo-flooring.co.uk  
Product reference: Forbo Eurocol 990 Europlan Direct
Application: Trowel or toothed smoothing trowel applied. Protect fresh layers against draughts and direct sunlight.
Where applying to an underfloor heated subfloor, the heating is to be turned off 24 hours before application and heat is not to be applied for at least 24 hours after application, in steps of 5°C per day.