To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

Allura Stone. A range of abstract, digital print and Uni colour design tiles providing a tough, resilient flooring surface suitable for the most demanding of situations. The Abstract designs represent a broad range of modern and in-vogue looks. These ranges offer a variety of designs from graphic metal designs to subtle textile effects. Colour and design combinations are further extended with a range of matching uni colours.

Dimensions: 50 x 50 cm; 75 x 75cm*
Thickness: 2.5 mm (0.7mm wear layer/0.55mm wear layer options).

Colours/ patterns: 19 standard designs/colourways.
Profile: Beveled (2 colourways) or Square*

* Dependent on colourway/design

Consult with Forbo technical literature for details.

110 TILING: VINYL.

Fabricated underlay:
Forbo QuickFit Subfloor System. – Optional.

Tiles: Vinyl to BS EN ISO10582.

Manufacturer: Forbo Flooring Systems Ltd, High Holborn Road, Ripley, Derbyshire, DE5 3NT.  Tel: 0800 0282 162 Fax: 01772 646912.  Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Allura Abstract.

BS EN ISO 10874 class: 34/43 (0.70mm) 33/42 (0.55mm) [delete as appropriate]
Size: 50cm x 50cm/75cm x 75cm[delete as appropriate].

Wearlayer Thickness: 0.70mm/0.55 mm [delete as appropriate].

Colour/ pattern: key: b = beveled edges;

50 cm x 50 cm – a63624/a63625/a63604(b)/a63603(b)/a63487/a63491/a63493/a63495/a63497/a63499/a63431/a63432/a63433/a63434/a60391/60393/

75 x 75cm – a63451/a63453/a63455

Adhesive (and primer if recommended by manufacturer):
Eurocol 540 Eurosafe Special - A superior acrylic dispersion solvent-free floor covering adhesive with a high initial grab for the installation of PVC tiles.
Eurocol 640 Eurostar Special – A superior acrylic dispersion very low VOC emission adhesive with a high initial grab  – to be specified where low emission adhesives are required for BREEAM section HEA9 credits are required 
Eurocol 140 Euromix PU - A polyurethane PU - A polyurethane resin and hardener, water-resistant 2-component PU-adhesive – to be specified in areas subject to abnormal temperature variations such as glazed window fronts.

Eurocol ‘646 Eurostar Premium - a very low emitting, moisture resistant adhesive. Wet set application method.

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.