To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

Allura Flex is a range of high quality, dimensionally stable, heterogeneous vinyl tiles that have been specifically designed for loose lay installation.

The subtle designs complement all types of spaces, providing a tough, resilient flooring surface suitable for the most demanding of situations.

Dimensions: 50 x 50cm; 100 x 100cm; 100 x 20cm; 120 x 20cm; HP 120 x 20cm; 150 x 28cm.*.
Thickness: 5 mm (1mm wear layer);

Colours/ patterns: 43 standard designs/colourways.
Edge Profile: Bevelled or Square*

* Dependent on colourway/design

Consult with Forbo technical literature for details.

110 TILING: VINYL.

Fabricated underlay: 
Forbo QuickFit Subfloor System. – Optional.

Tiles: Vinyl to BS EN ISO 10582

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, DE5

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Allura Flex.

BS EN ISO 10874 class: 34 / 43

Size: 50 x 50cm; 100 x 100cm; 100 x 20cm; 120 x 20cm; HP 120 x 20cm, 150 x 28cm [delete as appropriate].

Thickness: 5 mm

Colour/ pattern: Key: 4b = 4 sided bevel, 2b = 2 sided bevel length

50 x 50 cm; 1628/1633/1632/1634/9004/1656/1508/1506/1664/1584/9011/9013/9015/9017

100 x 100cm: 1624/1623/1626/1639/

100 x 20cm: 1535(4b)/1532(4b)/9050(4b)/9053(4b)/9056(4b)/1641/1644/1651/

120 x 20cm: 1605/1604/1682(4b)/1684(4b)/9073(4b)/9074(4b)/9075(4b)/9076(4b)/

HP 120 x 20cm: 9051(2b)/9054(2b)/9057(2b)

150 x 28cm: 1671(4b)/1670(4b)/1672(4b)/1674(4b)/9080(2b)/9084(2b)/

Adhesive (and primer if recommended by manufacturer): 542 Eurofix Tack Plus.

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.