To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

Allura Flex is a range of high quality, dimensionally stable, heterogeneous vinyl tiles that have been specifically designed for loose lay installation.

The subtle designs complement all types of spaces, providing a tough, resilient flooring surface suitable for the most demanding of situations.

Dimensions: 50 x 50cm; 75 x 50 cm;100 x 20cm; 120 x 20cm.*.
Thickness: 5 mm (1mm wear layer);

Colours/ patterns: 36 standard designs/colourways.
Edge Profile: Bevelled or Square*

* Dependent on colourway/design

Consult with Forbo technical literature for details.

110 TILING: VINYL.

Fabricated underlay: 
Forbo QuickFit Subfloor System. – Optional.

Tiles: Vinyl to BS EN ISO 10582

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, DE5

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Allura Flex.

BS EN ISO 10874 class: 34 / 43

Size: 50 x 50cm; 75 x 50 cm; 100 x 20cm; 120 x 20cm [delete as appropriate].

Thickness: 5 mm

Colour/ pattern: Key: b = beveled edges

50 cm x 50 cm; 1505/1508/1509/1541/1542/1543/1544/1584/1586/1589/1590/1592/1632/1633/1634/

1636/1656/1664

75cm x50cm: 1516/1517/1524/1578

100 x 20cm: 1641/1642/1644/1646/1647

120 x 20cm: 1556b/1557b/1564/1604/1678b/1679b/1681/1682b/1684b

Adhesive (and primer if recommended by manufacturer): 542 Eurofix Tack Plus.

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.