To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

Allura Premium. A unique range of designs inspired by nature and the expression of materials. The subtle designs complement all types of spaces, providing a tough, resilient flooring surface suitable for the most demanding of situations.

Dimensions: 50 x 15cm; 75 x 50 cm;100 x15cm; 120 x 20cm; 150 x28cm;100 x 100cm.*.
Thickness: 2.5 mm (0.7mm wear layer); 2.2mm (0.55mm wear layer).

Colours/ patterns: 16 standard designs/colourways.
Edge Profile: Square

* Dependent on colourway/design

Consult with Forbo technical literature for details.

110 TILING: VINYL.

Fabricated underlay: 
Forbo QuickFit Subfloor System. – Optional.

Tiles: Vinyl to BS EN ISO 10582

Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Allura Premium.

BS EN ISO 10874 class: 34 / 43

Size: 50 x 15cm;75 x 50 cm;100 x15cm;120 x 20cm;150 x28cm;100 x 100cm[delete as appropriate].

Thickness: 2.5 mm [delete as appropriate].

Colour/ pattern:

50 cm x 15 cm; w60129

75cm x50cm: w60242/w60244/w60246

120 x 20cm: w60126/w60127/w60128/w60233/w60235/w60237

150 x 28cm: w60110/w60112/w60114

100 x 100cm: s62337/s62339

Adhesive (and primer if recommended by manufacturer):
Eurocol 540 Eurosafe Special - A superior acrylic dispersion solvent-free floor covering adhesive with a high initial grab for the installation of PVC tiles.

Eurocol 640 Eurostar Special – A superior acrylic dispersion very low VOC emission adhesive with a high initial grab – to be specified where low emission adhesives are required for BREEAM section HEA9 credits are required 
Eurocol 140 Euromix PU - A polyurethane PU - A polyurethane resin and hardener, water-resistant 2-component PU-adhesive – to be specified in areas subject to abnormal temperature variations such as glazed window fronts.

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.