To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Surestep Wood Decibel: A range of heterogeneous safety vinyl floor coverings, with an acoustic foam backing and high-density calendared wear layer incorporating hard particles for enhanced slip resistance.

Surestep Wood Decibel meets the requirements of EN13845 for PVC floor coverings with particle based enhanced slip resistance and offers additional acoustic insulation with an excellent impact sound reduction of 17dB without concessions to the performance. Surestep Wood Decibel is suitable for use in Class 34, very heavy commercial use, areas.

Roll width: 2000 or 4000 mm.   Thickness: 3 mm.   Thickness of wear layer: 0.7 mm.
Colours/patterns:  8 x Wood designs

Matching welding rods are available in all collection colours.

Consult with Forbo technical literature for details.

150 SHEETING: VINYL

Fabricated underlay (delete where not required)                                                                                                                         Forbo QuickFit Subfloor System. – Optional.

Flooring roll:  Heterogeneous PVC to BS EN 651.

Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Surestep Wood Decibel.

Select from the following colours: 718322/718222/718442/718162/71892/718912/718722/718052

BS EN 685 class: 34 / 42
Width: 2000 / 4000mm [delete as appropriate]
Thickness: 3 mm.
Colour/ pattern: As finishes schedule

Adhesive (and primer if recommended by manufacturer):
Eurocol 540 Eurosafe Special – A superior acrylic dispersion solvent-free floor covering adhesive with a high initial grab.
Eurocol 640 Eurostar Special – A superior acrylic dispersion low VOC emission adhesive with a high initial grab.
Eurocol 233 Eurosol Contact – A synthetic rubber in solvent fast setting contact adhesive.

Seam welding: Hot welding with matching coloured rod.

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polished finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.