To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

130 CARPET TILE:

Tessera Earthscape: A tufted multi-height loop pile carpet tile. Manufactured with 100% solution dyed polyamide 6, on polyester primary and a modified bitumen and polyester secondary backing. Also available in SOFTbac®.

SOFTbac® is an additional backing layer which also acts as an underlay and offers increased sound and thermal insulation and extends the guarantee period by 50% to 15 years.

Tile size: 50 x 50cm, other sizes are available for special orders.

Pile weight: 978g/sm ± 10%

Thickness: 7.1mm ± 10%; With SOFTbac® + 3mm ± 10%.

Earthscape is available in 12 colourways.

Tessera carpet tiles must be laid in accordance with best practice techniques as detailed in the Contract Flooring Association’s guidelines and BS5325. Consult with Forbo technical literature for further details.

130 CARPET TILE:

Manufacturer: Forbo Flooring UK Ltd, High Holborn Road, Ripley, Derbyshire, DE5 3NT.

Tel: 01773 744 121 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Tessera Earthscape

Type: Tufted multi-height loop pile carpet tile

BS EN ISO 10874 classification: Class 33

Level of use class: Heavy Contract

Size: 50 x 50cm

Colour/ pattern: [select from] 3250 / 3251 / 3252 / 3253 / 3254 / 3255 / 3256 / 3257 / 3258 / 3259 / 3260 / 3261

Method of Laying: Monolithic or quarter turn

Adhesive: 542 Eurofix Tack Plus

Accessories: Edging and cover strips, as clause 740.