To complete the clause, select the appropriate wording from below.  Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER / PLASTICS / CORK / LINO / CARPET TILING / SHEETING

M50 SHEETING………..

Sarlon® 17dB: An acoustic floor covering with a certified impact sound reduction of 17dB, and a residual indentation level of just 0.09mm. No polishing will be necessary throughout the life of the covering.

Roll width:  2000mm. Thickness: 3mm.  Thickness of wear layer:  0.67mm                                                 Colours:  Linen - 10 standard colourways; Nuance – 15 standard Colourways; Wood – 13 Standard Colourways			                                                                                                                Matching welding rods are available in all collection colours                                                                  Consult with Forbo technical literature for details.

150 SHEETING: VINYL

Fabricated underlay: 
Forbo QuickFit Subfloor System. – Optional.

Flooring roll: Heterogeneous PVC to BS EN 651.
Manufacturer: Forbo Flooring UK Ltd, PO Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo Sarlon 17dB
BS EN 685 class: 34 / 42
Width: 2000 mm
Thickness: 3mm

Colour / pattern: [select from]

Linen - 436514 Taupe/436501 Pearl/436519 Dark Grey/436529 Anthracite/436502 Light Grey/436509 Medium Grey/436557 Dark Blue/436500 Ivory/436503 Beige/436544 Chocolate

Nuance – 436612 Light Grey/436619 Medium Grey/436666 Red/436603 Beige/436608 Pistachio/436658 Green/436611 Grey Beige/436614 Taupe/436624 Chocolate/436601 Pearl/436639 Dark Grey/436699 Black/436607 Grey Blue/436637 Blue/436647 Dark Blue.

Wood Large Country – 436162 Medium/436163 Light;

Wood all over - 436223 Ecru/436252 Dust/436222 Carbon.

Wood medium Classic – 436393 Light/436383 Natural/436334 Medium Oak/436394 Dark.

Wood Small Classic – 436234 Medium/436213 Natural/436214 Golden/436233 Honey.

Adhesive (and primer if recommended by manufacturer):
Eurocol 540 Eurosafe Special – A superior acrylic dispersion solvent-free floor covering adhesive with a high initial grab Specifiy for general purpose use.
Eurocol 640 Eurostar Special – A superior acrylic dispersion low VOC emission adhesive with a high initial grab – specify where BREEAN section HEA9 credits are required..
Eurocol 140 Euromix PU – A polyurethane resin and hardener, water-resistant 2-component PU-adhesive. – Specify where extremes of temperature or very heavy rolling loads are expected.
Seam welding: Hot welding with matching coloured rod.

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish

Other requirements:  Seek advice from Forbo for specific requirements for flooring

460 SMOOTHING/LEVELLING UNDERLAYMENT COMPOUND

Forbo Flooring in association with Eurocol manufacture a range of smoothing underlayment compounds. 
Forbo Eurocol 920 Europlan Alphy
Forbo Eurocol 975 Europlan Special
Forbo Eurocol 990 Europlan Direct

Forbo Eurocol 920 Europlan Alphy
A self-smoothing, tension-free hardening leveling compound for stony subfloors and especially for anhydrite subfloors and designed for leveling in layers between 0.5 and 30mm thickness.
Smooth and impervious subfloors (ceramic, granolithic, terrazzo), asphalt and bituminous floors to be primed with 044 Europrimer Multi. Highly absorbent subfloors to be primed with 044 Europrimer Multi or 049 Europrimer ABS. See clause M50/10 and 20 ‘Preparation’ for details.
Consult Forbo Flooring Ltd’s technical literature for details.

Type: Water/powder mix 
Manufacturer: Forbo Flooring UK Ltd, PO Box 1, Kirkcaldy, Fife KY1 2SB 
Tel: 0800 0282 162 Fax: 01772 646 912 
E-mail: info.flooring.uk@forbo.com Web: www.forbo-flooring.co.uk 
Product reference: Forbo Eurocol 920 Europlan Alphy
Application: Trowel or toothed smoothing trowel. Protect fresh layers against draughts and direct sunlight.
Where applying to an underfloor heated subfloor, the heating is to be turned off 24 hours before application and heat is not to be applied for at least 24 hours after application, in steps of 5°C per day.


Forbo Eurocol 975 Europlan Special
A self-smoothing leveling compound for stony subfloors and designed for leveling in layers up to 8mm thickness.
Smooth and impervious subfloors (ceramic, granolithic, terrazzo), asphalt and bituminous floors to be primed with 044 Europrimer Multi. Highly absorbent subfloors to be primed with 044 Europrimer Multi or 049 Europrimer ABS. See clause M50/10 and 20 ‘Preparation’ for details.
Consult Forbo Flooring Ltd’s technical literature for details.

Type: Water/Powder mix
Manufacturer: Forbo Flooring UK Ltd, PO Box 1, Kirkcaldy, Fife KY1 2SB 
Tel: 0800 0282 162 Fax: 01772 646 912 
E-mail: info.flooring.uk@forbo.com Web: www.forbo-flooring.co.uk 
Product reference: Forbo Eurocol 975 Europlan Special
Application: Trowel or toothed smoothing trowel applied. 
Where applying to an underfloor heated subfloor, the heating is to be turned off 24 hours before application and heat is not to be applied for at least 24 hours after application, in steps of 5°C per day.

Forbo Eurocol 990 Europlan Direct
A self-smoothing very high quality leveling compound especially suitable for critical for stony subfloors and designed for leveling in layers up to 20mm thickness.
Smooth and impervious subfloors (ceramic, granolithic, terrazzo) to be degreased with 014 Euroclean and rinsed with water. They do not normally require to be primed. Porous subfloors do not require to be primed but highly absorbent subfloors to be primed with 044 Europrimer Multi. Highly absorbent subfloors to be primed with 044 Europrimer Multi or 049 Europrimer ABS. See clause M50/10 and 20 ‘Preparation’ for details.
Consult with Forbo Flooring Ltd if applying to asphalt and bituminous floors.
Consult Forbo Flooring Ltd’s technical literature for details.

Type: Water/Powder mix
Manufacturer: Forbo Flooring UK Ltd, PO Box 1, Kirkcaldy, Fife KY1 2SB 
Tel: 01590800 0282 162Fax: 01772 646 912 
E-mail: info@forbo-flooring.co.uk Web: www.forbo-flooring.co.uk 
Product reference: Forbo Eurocol 990 Europlan Direct
Application: Trowel or toothed smoothing trowel applied. Protect fresh layers against draughts and direct sunlight.
Where applying to an underfloor heated subfloor, the heating is to be turned off 24 hours before application and heat is not to be applied for at least 24 hours after application, in steps of 5°C per day.