To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

150 SHEETING: . . . . . .

Marmoleum Ohmex. Part of the Marmoleum Marbled collection, Marmoleum Ohmex is heavy duty static conductive linoleum floor covering designed for use in a wide variety of ESD installations – electronic manufacturing, pharmaceutical applications etc.

Marmoleum Ohmex meets the requirements of BS EN100 015 for floors (not required for grounding personnel). For floors (working areas) such as production facilities for ESD devices Marmoleum Ohmex delivers the required electrical performance. Marmoleum Ohmex is suitable for use where high voltage equipment, computers and sensitive electronic equipment are used. Marmoleum complies with IBM/ICL requirements.

Roll width: 2000 mm. Thickness: 2.5 mm. Standard colours: 6
Consult Forbo Flooring for details, samples and colour availability.

150 SHEETING: LINOLEUM

Flooring roll: Linoleum to BS EN ISO 24011
Manufacturer: Forbo Flooring, PO Box 1, Kirkcaldy, Fife KY1 2SB Tel: 01592 643777 Fax: 01592 643999 E-mail: info.uk@forbo.com Web: www.forbo-flooring.co.uk
Product reference: Marmoleum Ohmex 
BS EN 685 class: 23 / 34 / 42
Width: 2000 mm
Thickness: 2.5 mm
Colour/pattern: As finishes schedule

Adhesive (and primer if recommended by manufacturer): 
 Primer: Eurocol 041SC static conductive primer, roller applied to base (including top surface of copper strips) at rate of 7m²/litre. Allow to dry completely.
Adhesive: Eurocol 615 Eurostar Lino EL solvent free very low Emission Conductive Adhesive, V-notched trowel applied.

Seam welding: [select as required from below]

Hot welded with matching Marmoweld weld cable

Net fit seams not welded

Accessories: Electrical grounding: Copper strip(s), 10mm wide fixed to base using Eurocol 512SC static conductive adhesive, not less than on strip for each 36m² of floor area. Link to ground connection(s) supplied by others. Contact Forbo Flooring for further details.

Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish

Other requirements: 
Seek advice from Forbo for specific requirements for flooring.

# 770 Skirtings

# Type: Set in Skirting

Manufacturer and reference: Marmoform S / Marmoform SW Coving by Forbo-Nairn Ltd.

Size: 100 mm high x 50 mm toe.

Thickness: 2.5 mm

Colour/pattern: _________

Adhesive (and primer if recommended by manufacturer): Contact adhesive.

Securely bond with top edge straight and parallel with floor. Accurately mitre at corners except where pre-formed angles are used. All mitred and horizontal joints to be hot seam welded using matching Marmoweld weld cable (except where pre-formed angles are used). Vertical joints may be either hot seam welded or sealed with clear silicone sealant applied to the exposed edge of each section of skirting prior to sticking the next section of coving – contact Forbo Nairn for further details if required.

Type: Self coved skirting

Cove former: QCF35 35mm radius by Quantum Profiles tapered to architraves. Securely bond to base and background using contact adhesive. Accurately mitre at corners.

Top edge trim: UCS2 PVC capping strip by Quantum profiles. Securely bond to background using contact adhesive, with top edge straight and parallel with floor.

Turn flooring material up wall, securely bond to cove former and background using adhesive specified for fixing to base, and ease top of material into edge trim. Accurately mitre at corners. All joints to be hot welded in accordance with the manufacturer’s instructions.

Height: ______