To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

ColoRex® SD/EC. A high performance pressed PVC tile floor covering available in both static dissipative (electrical resistance 106 to 108 and static conductive (electrical resistance 5 x 104 to 1 x 106 Ω) variantsBesides offering ESD/ EMI protection, these Static Control tiles offer high resistance to wear and indentation, have excellent chemical resistance and fulfill the latest GMP regulations.

Pre-formed internal and external corners are available to use with pre-manufactured skirting strips where high hygiene requirements dictate the use of a coved skirting system.

Dimensions: 615 x 615 mm. Also available to special order 615 x 1230 mm (contact Forbo Flooring for further details).

Thickness: 2.0 mm. 3.0 mm is also available to order (contact Forbo Flooring for further details).                                                                            Colours/ patterns: EC - 21 standard colourway, SD - 25 standard colourways.
Consult with Forbo technical literature for details.

110 TILING: VINYL

Fabricated underlay: 
Forbo QuickFit Subfloor System. – Optional.

Tiles: Electrostatic and conductive vinyl
Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Product reference: Forbo ColoRex®. Select either Colorex SD or Colorex EC.
BS EN 685 class: 34 / 43
Size: 615 x 615 mm [standard] also available 610 x 610 mm / 615 x 1230 mm [made to order].
Thickness: 2.0 mm [standard] / 3.0 mm [made to order].
Colour/ pattern: As per finishes schedule
Adhesive (and primer if recommended by manufacturer): 
Static conductive system:
Eurocol 801 Copper-Strip - A static conductive copper earth strip                                                              Eurocol 641 Eurostar Special EL - A superior conductive acrylic dispersion very low VOC-emission (EC1) with a high initial grab.
Eurocol 141 Eurosafe PU EL - A conductive polyurethane resin and hardener, water-resistant, low VOC-emission (EC1) 2-component PU-adhesive.

Accessories:
Edging and cover strips, as clause 740.
Stair nosing, as clause 750.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.
An electrical discharge system is required; consult Forbo Flooring for detailed guidance on the requirements of the discharge system.

# 770 Skirtings

Type: Self coved skirting

Cove former: 20mm radius - Quantum Profile Systems – ECF2; www.quantumprofilesystems.com.

Top edge trim [delete if not required]: Quantum Profile Systems; www.quantumprofilesystems.com

Quantum Profile Systems UCS2 PVC capping strip [for use with a finished smooth wall]

Quantum Profile Systems QCT1 PVC capping strip [for use with PVC Cladding or ceramic tiled walls – fitted by other prior to the installation of the cladding/wall tiling]

Securely bond to background using contact adhesive, with top edge straight and parallel with floor.

Colorex preformed corners and pre-manufactured skirting strips

Finished height: 100mm

Manufacturer: Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk

Guidance notes:

Pre-formed corners and skirting strips should be fitted after the main field tiles have been installed

Fit pre-formed corners first, securely bond to background and floor using contact adhesive, and ease top of material into edge trim (if used). Trim overlap of the skirting foot to edge of field tiles.

Fit skirting strip up wall, aligned with top edge of pre-formed corners securely bond to cove former and background using contact adhesive and ease top of material into edge trim (if used). Trim overlap of the skirting on the floor to the edge of field tiles.

All joints to be hot welded in accordance with the manufacturer’s instructions.

For more detailed installation guidance refer to manufacturer’s website: www.forbo-flooring.co.uk