To complete the clause, select the appropriate wording from below. Highlighted text can be ‘dragged and dropped’ to save typing.

M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING

110 TILING: . . . . . .

ColoRex® R11 Plus. A high performance loose lay interlocking PVC tile floor covering with a profiled surface for added grip. Suitable for use in very heavy commercial areas and in industrial areas where fork trucks are in operation, these tiles offer high resistance to wear and have excellent chemical resistance.

Dimensions: 608 x 608 mm.                                                                                                          Thickness: 10.5mm                                                                                                                                   Colours/ patterns: - 1 standard colourway.
Consult with Forbo technical literature for details.

110 TILING: VINYL

Fabricated underlay: N/A

Tiles: Loose lay vinyl
Manufacturer:   Forbo Flooring UK Ltd, P O Box 1, Kirkcaldy Fife, KY1 2SB.

Tel: 0800 0282 162 Fax: 01772 646912

Email: info.flooring.uk@forbo.com. Web: www.forbo-flooring.co.uk 
Product reference: Forbo ColoRex® R11 Plus.
BS EN 685 class: 34 / 43
Size: 608 x 608 mm.
Thickness: 10.5 mm.
Colour/ pattern: 601060
Adhesive (and primer if recommended by manufacturer): N/A

Seam Welding: N/A

Accessories:
Edging and cover strips, as clause 740.
Skirtings, as clause 770.

Finishing: As clause 820 omitting polish finish.

Other requirements: Seek advice from Forbo for specific requirements for flooring.